## Slide 1: CAN bus
Matthew Whitworth

## Slide 2: What is the CAN bus?
Controller Area Network
Twisted pair of wires connecting all nodes within a system
  Effectively one signal from two wires
Nodes refer to ECUs such as motor controllers, BMS or the MoTeC

## Slide 3: What are the benefits?
Industry standard
Resilient to noise
High speed data transmission
Greatly simplifies wiring

## Slide 4: How it works - Hardware
Differential Signalling
Difference between high and low signals provides logical output
Dominant 0 system; 0’s overpower 1’s
Logical 0 when CANH high and CANL low
Noise present on both lines effectively subtracted out, CANH - CANL

## Slide 5: How it works - Hardware
CAN Bus Node Layout
Transceiver performs differential process and sends/receives noise free signal to/from controller
Controller stores sent or received messages from the MCU or bus until the bus is free or the MCU requests a stored message

## Slide 6: How it works - software
Extended CAN Message structure
Concerned with only data and ID sections
Extended gives 29 bit ID length instead of 11
Data typically treated as 8 separate bytes
  More bytes for higher resolution data
Message Byte data example |  |  |  |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Throttle Position |  | Front Brake Pressure |  | Rear Brake Pressure |  | Brake switch | Trail Brake

## Slide 7: How it works - software
Message Prioritisation
Priority based messaging
  Smaller ID’s are of a larger priority
CAN controllers operate in sync
Dominant logical 0’s effectively stop lower priority nodes from transmitting
 | Binary ID |  |  |  | Decimal ID
Node 1 | 0 | 1 | 0 | 1 | 5
Node 2 | 0 | 0 | 1 | 0 | 2
Node 1 stops transmitting when it detects a dominant 0 overwriting its recessive 1

## Slide 8: How it works - software
Code Implementation
FlexCAN_T4 library
Only need to define message ID and content and library will handle the rest
Refer to datasheets to interpret CAN messages from OTS components

## Slide 9: EV2 Implementation
Controllers share ID’s
Controllers and BMS operate at different baud rates
Interfaces required to change ID’s and baud rate to be put onto main bus

## Slide 10: EV3 Plan